BUILD A PINHOLE CAMERA

1-Build a Pinhole Camera

Making the box light-tight is the hard part. The job of making a light-tight box is

simplified by getting a well-built box with a deep fitting lid  or a can with a lid.

Materials Needed:

Box or can (can is preferable)

Black gaffer tape and electrical tape

Glue

Small needle

Exacto knife

Black semi-flat paint - krylon spray if using a can

Aluminum foil

A. Paint the inside of the box black, because black absorbs light rays. Use black

construction paper or gaffer tape (easier to adhere) to cover any seams or

openings and ensure a light-tight box or can.

B. Make a square hole in the center of one side of the box where will be the

"lens".

C. Drill the tin foil with a needle to make a very small hole.

D. Tape the aluminum foil over the square hole on the inside of the box with

black electrical tape.

E. Cover  the pinhole, with a piece of  electrical tape to act as the "shutter".

Make sure you fold it over at the button end of the tape to make it easier to

move it up and down when you're photographing.

2- Creating an Image

A. Working in a darkroom or changing bag, place photographic paper inside

the camera, with the emulsion ( shining side of the paper) facing the

pinhole.

B. Secure the tape around the edges of the camera and keep the "shutter"

closed as you take the camera to the light.

C. Expose the paper by lifting the "shutter" (flap). Remember to record your

exposure time because it takes some testing to get the right exposure!

D. Set up the trays with Developer, Stop ,Fixer and Water.

Developer -gentle agitation for  1 to 1:30 min

Stop - gentle agitation for 15 sec

Fixer - gentle agitation for 1 to 2 min

Wash running water for 5 min

Those times are for Ilford chemistry and  Ilford RC paper.

E. Hang prints to dry with clothe pins.

Images from Photography In Focus: Basic Text, by Jacobs